Reflash WiFI-modul with uStepper GUI

Install the ESP8266 package for Arduino IDE:
https://github.com/esp8266/Arduino
Board file: http://arduino.esp8266.com/stable/package_esp8266com_index.json

Download and install ArduinoWebSockets (can be downloaded through Arduino IDE) https://github.com/Links2004/arduinoWebSockets

Download and install the ESP8266 SPIFFS file uploader for Arduino (C:\Program Files (x86)\Arduino\tools): https://github.com/esp8266/arduino-esp8266fs-plugin

(optional) Connect a USB to TTL converter directly to the WiFi-module (VCC, GND, RX and TX). Open a Serial monitor and set the baud rate to 74880. You should see some boot information if you press the reset button (“right” button, blue arrow)

Now to upload software the board needs to be in flash-mode. To enable flash-mode turn off the power to the module, and repower it while holding down the “left” button (see red arrow). The module can now be programmed.

Select the board “Generic ESP8285 Module” and set the flash size to “1M (512K SPIFFS)”. Now Hit that upload button!’